## Slide 1: Travelling Salesperson Problem Hardware Accelertor
Presenter: 林修賢

## Slide 2: Outline
Problem Description
TSP Algorithm &Hardware & Its Optimization (Original Version )
TSP_DP Algorithm
TSP_DP Hardware Implementation
  Opt1_algorithm
  Opt2_double _array
  Opt3_col_partition
  Opt4_compress_memory
Analysis & Conclusion
https://github.com/showlin/2022NYCU-HLS-Lab-B---Travelling-Salesperson-Problem-Hardware-Accelertor

## Slide 3: Problem Description
Travelling salesman problem(TSP):
Given a list of cities and the distances between each pair of
cities, finding shortest possible route that visits each city
exactly once and returns to the origin city.
NP-hard problem, its time complexity is O(N!)

## Slide 4: TSP Algorithm (Naive)
Find all cities path permutations --> O( (N-1)! )
  Ex: There are cities 1 2 3.
  (3!) = 6 , (2!) = 2
  1->2->3 | 2->3->1 | 3->1->2 are same
  1->3->2 | 3->2->1 | 2->1->3 are same
Every path length need O(N) computation
  Ex: path 1->2->3 .
  Distance12+Distance23+Distance31
Total complexity is O(N!)

## Slide 5: TSP Hardware
Main
TSP kernel
TSP kernel
N*N
Distance
Shortest
Path
compute
N*N bram
distance0[N][N]
For( i =0; i<(n-1)!; i=i+1)
distance
min
Shortest
Path

## Slide 6: TSP Hardware
compute
N*N reg
distance0[N][N]
Index i
drcorder
permutation
accumulator
Ex: N=13 , index= 0
  Permutation is 1 2 3 4 5 6 7 8 9 10 11 12 13
Ex: N=13 , index= 479001599
  Permutation is 13 12 11 10 9 8 7 6 5 4 3 2 1

## Slide 7: TSP Hardware optimization
TSP kernel
Compute
N*N bram
distance0[N][N]
For( i =0; i<(n-1)!; i=i+2)
distance1
min
Shortest
Path1
N*N bram
distance1[N][N]
i
i+1
Compute
distance2
min
Shortest
Path2
min
Shortest

## Slide 8: TSP_DP Algorithm
Naïve TSP:
  Time complexity O(n!)
  Space complexity O(n^2)+O(1)
Observation
  We compute same permutation repeatedly
  We only care the last city of a segment of permutation.
  Complexity degrade from permutation to combination
DP TSP:
  Time complexity O(2^n * n^2)
  Space complexity O(2^n * n)
1 2
3 4 5 6
1 2
3 4 5 6
3 4 5 6
1
2
3 4 5 6
2
1
3456
3546
4356
4536
5346
5436
345
6
We only keep the minimum value of that combination
N=13
Naïve TSP: 6227020800
DP TSP : 1384448
Ideal 4500x speed up
(sw implement 4300x )

## Slide 9: TSP_DP Space complexity
DP TSP:
  Time complexity O(2^n * n^2)
  Space complexity O(2^n * n)
We use bit to present the number combination O(2^n)
  Ex: when N=3, 000={}, 001={0}, 010={1}, 011={0,1}…...111={0,1,2}
For every combination, we should record every bit for last bit situation O(n)
  Ex: when N=4, we know 1101 means {0,2,3}
So we need O(2^n)*O(n) space
02
3
23
0
03
2

## Slide 10: TSP_DP Time complexity
DP TSP:
  Time complexity O(2^n * n^2)
  Space complexity O(2^n * n)
How do we compute a block?
For every block, we cost O(N) to compute
02
3
2
0
0
2
distance03
distance23
min
Example : N=4,{0,2,3},last bit is 3

## Slide 11: Opt1_algorithm basic -ii2
TSP_DP kernel
reg
distance[N][N]
For( i =0; i<2^n; i=i+1)
min
Shortest
SRAM
v[2^N][N]
For( j =0; j<n; j=j+1)
For( k =0; k<n; k=k+1)
v[i][j] = min( v[i][j],v[~(~i | 1<<j)][k] + int(distance[j][k]) ) ;

## Slide 12: TSP_DP Memory access
DP TSP:
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[0][0]
V[0][1]
V[0][N-1]
V[1][0]
V[1][1]
V[1][N-1]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-2][0]
V[M-2][1]
V[M-2][N-1]
V[M-1][0]
V[M-1][1]
V[M-1][N-1]
V[2][0]
reg
distance[N][N]
V[2][1]
M: 0~2^n-1
N : 0~n-1

## Slide 13: Analysis
每次都對同塊記憶體做一次讀一次寫，所以必定要stall一次(ii=2)。
13^2*2^13大概是140萬，結果因為最內層ii=2，硬生生的變成280萬cycle....

## Slide 14: Opt2_double _array ii1
TSP_DP kernel
reg
distance[N][N]
For( i =0; i<2^n; i=i+1)
min
Shortest
SRAM
v0[2^N][N]
For( j =0; j<n; j=j+1)
For( k =0; k<n; k=k+1)
if( is_odd(i) ){
t = std::min(t,v0[~(~i | 1<<j)][k] + int(distances[j][k]) ) ;
v1[i][j] = t;
}
else{
t = std::min( t,v1[~(~i | 1<<j)][k] + int(distances[j][k]) ) ;
v0[i][j] = t;
}
SRAM
v1[2^N][N]

## Slide 15: TSP_DP Memory access
DP TSP:
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V1[0][0]
V1[0][1]
V1[0][N-1]
V1[1][0]
V1[1][1]
V1[1][N-1]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V1[M-2][0]
V1[M-2][1]
V1[M-2][N-1]
V1[M-1][0]
V1[M-1][1]
V1[M-1][N-1]
V1[2][0]
reg
distance[N][N]
V1[2][1]
M: 0~2^n-1
N : 0~n-1
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V0[0][0]
V0[0][1]
V0[0][N-1]
V0[1][0]
V0[1][1]
V0[1][N-1]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V0[M-2][0]
V0[M-2][1]
V0[M-2][N-1]
V0[M-1][0]
V0[M-1][1]
V0[M-1][N-1]
V0[2][0]
V0[2][1]

## Slide 16: Analysis
我發現每次讀跟寫memory的address都差1bit，所以我直接複製用一塊記憶體，就不會每次讀寫都產生stall了
雖然有一些overhead，但實際值1695382跟理論上最佳化([2^N]*N*N,N=13) =1384448，算是同一個量級的

## Slide 17: Opt3_col_partition
TSP_DP kernel
Bram
distance[N][N]
For( i =0; i<2^n; i=i+1)
min
Shortest
SRAM
v0[2^N][N]
For( j =0; j<n; j=j+1)
SRAM
v1[2^N][N]

## Slide 18: TSP_DP Memory access
DP TSP:
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V1[0][0]
V1[0][1]
V1[0][N-1]
V1[1][0]
V1[1][1]
V1[1][N-1]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V1[M-2][0]
V1[M-2][1]
V1[M-2][N-1]
V1[M-1][0]
V1[M-1][1]
V1[M-1][N-1]
V1[2][0]
reg
distance[N][N]
V1[2][1]
M: 0~2^n-1
N : 0~n-1
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V0[0][0]
V0[0][1]
V0[0][N-1]
V0[1][0]
V0[1][1]
V0[1][N-1]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V[M-1][0]
V0[M-2][0]
V0[M-2][1]
V0[M-2][N-1]
V0[M-1][0]
V0[M-1][1]
V0[M-1][N-1]
V0[2][0]
V0[2][1]

## Slide 19: Analysis
我把loop3 unroll後，他也自動幫我把loop2 unroll了，原本每次loop 2要花169cycle，現在每次只要花20cycle，理論上我切成13塊，如果可以完全平行就可以降成13，但在loop轉換時會有一些data dependency的over heap，那個是沒辦法消除了。
理想值([2^N]*N*N/N,N=13)=106,496 跟我們實際172030其實是一樣量級，因為沒有完全平行，且當計算量越小時，memory 初始化所花的時間就會比較顯著。

## Slide 20: Memory utilization
(優化4時的使用資源)
(優化3時的使用資源)
Compress array by encoding address

## Slide 21: Opt4_compress_memory
TSP_DP kernel
Bram
distance[N][N]
For( i =0; i<2^n; i=i+1)
min
Shortest
SRAM
v0[2^N][N]
For( j =0; j<n; j=j+1)
SRAM
v1[2^N][N]

## Slide 22: Speed up
幫我第二層loop自動做unloop，20 cycle -> 9 cycle
總時間也從剛剛的1.716E6 s 變成7.78E5 s

## Slide 23: Conclusion
Software
  1.naive version : 43.71s
  2.Dp version : 0.01s
Hardware
  Baseline_Reference : 1.4s
  Optimal_Reference : 0.1s
  V1 : 0.028s
  V2 : 0.017s
  V3 : 0.0017s
  V4 : 0.00078s
Conclusion
  My best design TSP_V4 is 13X faster then software dp_tsp, 141X fast then hardware Optimal_Reference.

## Slide 24
Thanks for your listening.